## Slide 1
The ACE/MAG Experiment
Norman F. Ness, Mario H. Acuna,
Leonard E. Burlaga, Jacques L’Heureux, John Scheifele and Charles W. Smith

## Slide 2
The ACE/MAG Experiment
Norman F. Ness1, Mario H. Acuna2,
Leonard E. Burlaga2, Jacques L’Heureux1,
John Scheifele2 and Charles W. Smith1
1. Bartol Research Institute/U. of Delaware
2. Goddard Space Flight Center/NASA

## Slide 3
Purpose:
To record the local magnetic field in which the ACE particle measurements are made.
  To permit refined interpretation of particle observations including distribution functions relative to the ambient magnetic field.
To combine with the thermal particle instruments in providing a refined dataset for the study of interplanetary plasma dynamics.
To serve as a real-time solar wind monitor for NOAA’s space weather forecasting.

## Slide 4
Hardware:
Twin triaxial fluxgate magnetometer of IMP, Mariner, Voyager and MGS heritage.
Fully redundant sensors and electronics.
On-board buffering of select, high-resolution data.

## Slide 5
Heritage and Configuration:
ACE/MAG is the WIND/MFI spare fluxgate magnetometer made compatible with the ACE spacecraft.
Twin triaxial sensors are deployed on two opposing booms 4.2 meters from the center of the spacecraft (3.3 m from side).

## Slide 6
Configuration (cont’d):
Non-magnetic boom materials with good thermal properties reduce fields due to thermal currents.
Sensors are covered by thermal blankets.
MAG activation and deployment is 1 hour after launch in low-altitude magnetosphere.

## Slide 7
Performance:
The instrument provides continuous three-component vector averages of the magnetic field with 3, 4 or 6 vector/second resolution.
On-board FFT buffers extend the spectral resolution of averaged data to 12 Hz.
Dual 297 second on-board snapshot buffers with 24 vector/second resolution capture high-frequency transient phenomena.

## Slide 8
Characteristics:
Eight dynamic ranges: ± 4, ± 16, ± 64, ± 256, ± 1024, ± 4096, ± 16,384 and ± 65,536 nT
Digital resolution (12 bit): ± 0.001, ± 0.004, ± 0.016, ± 0.0625, ± 0.25, ± 1.0, ± 4.0 and ± 16.0 nT
Bandwidth: 0 to 12 Hz
Sensor noise level: < 0.006 nT RMS
Sensitivity: ~ 0.0005 nT/Hz in most sensitive range

## Slide 9
Characteristics (cont’d):
Mass:
  Sensors (2): 225 g each
  Electronics (redundant): 2100 g total
Power consumption:
  Electronics: 2.4 watts, regulated 28 volts +/-2%
  Heaters: 1.0 watts, unregulated 28 volts

## Slide 10
Spacecraft Magnetics:
Magnetic goals have been supported by APL and the instrument teams through an informal program of design and measurement.
No AC magnetic noise > 0.1 nT has been identified in preliminary ground measurements.
Present DC field is estimated at < 1 nT at each sensor location. Final compensation of spacecraft remains an option.

## Slide 11
Science Opportunities:
Interplanetary propagation of solar and galactic energetic particles including charge, species and isotope dependence.
Study of in situ acceleration of solar and interstellar particles including pickup ions.
Study of interplanetary turbulence and solar wind transients in collaboration with thermal particles instruments and other instrument teams.

## Slide 12
Science Opportunities (cont’d):
Coordinated studies of the solar wind with IMP-8, Voyagers, Ulysses, Mars Global Surveyor, SOHO, etc.
  Solar wind studies during both solar minimum and maximum.
Coordinated studies with ISTP spacecraft, including WIND.
Space weather forecasting using ACE as an upstream monitor of the solar wind.

## Slide 13
Summary:
The ACE/MAG instrument is a state-of-the-art triaxial fluxgate magnetometer with on-board snapshot and FFT buffers.
No impediments to data quality foreseen.
The ACE/MAG instrument is integrated with the spacecraft and ready to fly.
Additional information is available at: http://www.bartol.udel.edu/